## Slide 1: OP-AMP Design
ECEE 421
Ho Wang Lam

## Slide 2: Overview and Intro
Reconstructing the LM741 with npn 2N2222 and pnp 2N2907 and analog parts
Assuming electrical characteristics (Early voltage, beta, reverse saturation current of transistors, etc.) of the components are similar to the real npn 2N2222 and pnp 2N2907

## Slide 3: Circuit Breakdown

## Slide 4: Setup
Vin of 40mVpp sin wave at 5000Hz
V+ of 15V
V- of -15V
Rf = 5k
Rin = 2.5k
Expecting gain:
Rf/Rin = -2 V/V

## Slide 5: Compare to real LM741

## Slide 6: Bias Circuit– Referent Current
Two diode-connected transistors Q11 and Q12 and the resistance R5
Create a Iref in the center and other stages can use this and current mirrors to refence them self

## Slide 7: Input stage - Differential Input
Q10 mirrors Q11 and delivers it to Q3 and Q4 base
Q1 and Q2 act as emitter followers, causing the input resistance to be high and delivering the differential input
Q3 and Q4 act as differential common-base amplifier and delivering to loading circuit.
Q5, Q6, and Q7 and resistors R1, R2, and R3 form the load circuit of the input stage.
  Provides gain
  Output is taken at Q6 collector

## Slide 8: Stage 1 output – 40mVpp input

## Slide 9: Stage 1 output 2Vpp input

## Slide 10: Voltage Gain Stage - 1
Signal from Stage 1 is feed into Q18 base
Q17, Q18 form a Darlington pair to achieve and bate^2 and have a high gain
Q18 is emitter follower
  High Rin
  Prevent gain loss
Q17 common emitter amplifier
  Load of Q17 is active load formed by pnp Q12, Q13

## Slide 11: Voltage Gain Stage - 2
The Darlington Pair with active load forming a Class A amplifiers
Q12,Q13 Current mirror acting as active loading to achieve high resistance
Rout of the current mirror:
Q17, Q18 form a Darlington pair to achieve and bate^2 and have a high gain
Example of Class A amplifier
Source: www.electronics-tutorials.ws

## Slide 12: Voltage Gain Stage - 3
30pF cap is feedback know as Miller compensation and create a dominant pole compensation and give a pole as low as 10 Hz -3dB cutoff
Output of gain stage is at Q17 collector

## Slide 13: Stage 2 output

## Slide 14: Output Stage - 1
Goal of the stage is to provide a low Rout and able to supply a large load current
Class AB output stage formed by Q14 and Q20 and bias by Q16 and R7 and R8
Output of the OPAMP is between R9, R10
Ideally Q14, Q20 should have a larger area for supplying higher loading current and minimal temperature effect

## Slide 15: Class AB output stage example

## Slide 16: Output Stage - 2
Short circuit protection Q15 limit the current go to Q14
The book example has a extra pnp to protect Q20, however on the datasheet the protection for the sink does not exist

## Slide 17: Difference between textbook and datasheet

## Slide 18: Performance Compare – 40mVpp Input 0V offset Application In An Inverting Amplifier

## Slide 19: Performance Compare – 2Vpp Input 1V offset Application In An Inverting Amplifier Rf 5K Rin 2.5k

## Slide 20: DC analysis - 1
Caps are open circuits
Short all input signals

## Slide 21: DC analysis - 2

## Slide 22: DC analysis - 3

## Slide 23: Performance Compare - Frequency Response

## Slide 24: Performance Compare - Frequency Response Stage 1

## Slide 25: Performance Compare - Frequency Response Stage 2

## Slide 26: Performance Compare - Voltage Swing
DC vin from -10 to 10
Expecting gain of -2 since Rf/ Rin = 5k/2.5k

## Slide 27: Performance Compare - Voltage Swing

## Slide 28: Performance Compare – Voltage Swing My 741

## Slide 29: Performance Compare – Voltage Swing Zoomed In
DC vin from -10 to 10
Expecting gain of -2 since Rf/ Rin = 5k/2.5k
Not as good as real 741 but still within datasheet range

## Slide 30: Electrical Characteristics

## Slide 31: Input offset Input offset voltage Vos - 2

## Slide 32: Input offset voltage Vos - 2
My 741 Vos = 568.3mV / 2 = 284mV
Real 741 Vos = 19.17mV / 2 = 9.58mV

## Slide 33: Input Bias Current, Positive Terminal, IB2 - 1

## Slide 34: Input Bias Current, Positive Terminal, IB2 - 2
My 741 Ib2 = -93.08pV / (1M(1+1k/100)) = 8.4uA
Real 741 Ib2 = 291.5uV / (1M(1+1k/100)) = 26.5pA

## Slide 35: Input Offset Current IOS - 1

## Slide 36: Input Offset Current IOS -2
The datasheet value for IOS is given as typically 2 nA and maximum 20 nA under ideal temperature conditions. Using this value, the maximum value of Vout can be calculated given that Rf =1 MΩ.
Vout = Rf (IOS)
Voutmax = (1 MΩ)(20 nA) = 20 mV
The computed value of IOS was calculated using the measured Vout of the circuit with R1=100 kΩ, Rf=1 MΩ, and R2=R1||Rf=91 kΩ

## Slide 37: Input Offset Current IOS - 3
The datasheet Ios: Typical 2 nA and maximum 20 nA
My 741 Ios = -7.892mV/1M = 7.89nA
Real 741 Ios = -7.235mV/1M = 7.24nA

## Slide 38: Common mode Rejection

## Slide 39: Slew Rate
Slew Rate = 2* π *f*V
f = the highest signal frequency, Hz V = the maximum peak voltage of the signal
Cutoff around 33kHz
2 π x 33 000 x 2 = 0.414744 V/µs

## Slide 40: CMOS low power OPAMP

## Slide 41: Bias circuit

## Slide 42
Input stage - Differential Input -1

## Slide 43
Input stage - Differential Input
Biased by current source Q5
Differential pair Q1–Q2
Current-mirror load Q3–Q4

## Slide 44: Out put Stage – Common-Source Amp
common-source transistor Q6
current-source load Q7.
frequency compensating the op amp Cc

## Slide 45: Output Rf = 5k, Rin = 5k, Vin 40mVpp

## Slide 46: Output Rf = 5k, Rin = 2.5k, Vin 40mVpp

## Slide 47: Performance - Frequency Response

## Slide 48: Performance - Voltage Swing